DEEP LEARNING FOR SELF DRIVING CARS

STRATO-IT

BY

SUDARSHAN KAMATH

KAUSTUBH VYAS

ANURAG SONTHALIA

ABSTRACT

Deep Learning has often been used in self driving vehicles on the roads as well as in the industries. Image classification benchmarks have been established quite popularly using neural networks. We realize the underlying potential of neural networks and hence aim to create a line following RC car using deep learning techniques. We shall be using the video obtained through an FPV camera for input. There are various approaches to this problem. We shall be going through those, while justifying why we approached the problem using a simple fully connected neural network. We would also be describing the difficulties that we made and the mistakes that you could make and hence be on a lookout for. In the end, we would be describing the results and would also provide a few points for improvement over our model.

METHODOLOGY

We have used the following approach to this problem in order to gain an optimum solution :

1. Try and achieve complete control over the RC car’s throttle and steer though a command line interface or PC control
2. Attach camera on the car at a suitable position and code it to run simultaneously with the car
3. Use the camera and the car to gain training data for the ML/DL model
4. Find potential models which can be trained with the help of this data
5. Train model and then test it
6. Find scopes for improvement and try and improve accuracy of model.
7. If step 6 does not work, then try another model

We would be describing each of these steps in detail throughout this document.

HARDWARE

We have used the following hardware for the project :

1. Arduino Uno x 1
2. Connecting wires
3. M to F / M to M / F to F converter wires
4. Wifi Shield for Arduino JSN270
5. Oscilloscope
6. Brown board
7. Soldering apparatus

SOFTWARE AND GPU

The entire code ran on a Intel-Core i5-8400 CPU with clock speed of 2.80Ghz with 6 cores. The GPU is a Nvidia GeForce 1050 Ti. We used UBUNTU Debian 16.04 operating system.
The codebase was entirely written in python 2.7.13 installed with the help of anaconda version 4.4.0. OpenCV version was 2.4.11. CUDA v8.0.61 for python2, 64bit was used. Sketch was used to write the code for arduino. We will mention about the other packages as we encounter them during the description of the code. Do check the references in the end for the complete code.
SKETCH CODE :

Sketchbook was used to make the code which ran the arduino. The JSN270 wifi shield provided connectivity with the laptop. A client code was written which first connected to the WiFi and then searched for a server with a given IP address. A web server(Listener) was started on the laptop/PC with the same IP address and PORT number. Once connection was established, we could give control commands from the command line to the arduino.

Initially an attempt was made to connect with the PC using bluetooth. However connectivity was sketchy and not stable. We used a Jarduino with an inbuilt bluetooth module for the same. We received a lot of garbage values in the bluetooth buffer and a lag in command sending and receiving. Hence we decided to reject it.

There was a radio receiver attached to the RC car, which received signals from the remote control and then sent PWM signals to the on-board controller of the car. We removed this radio receiver and used the arduino as a receiver of command line signals. The arduino would then interpret this signals and provide the suitable PWM signals to the steer and throttle control motors.

The required values of the PWM signals were first measured with the help of an oscilloscope attached to the radio receiver.

The remote control provided an almost continuous range of steer angles and throttle speeds, including the ability to reverse. We decided that we did not require such excessive functionalities in our car for this project. Hence we made it possible to iterate back and forth over a few discrete steer angle values which provided us enough control over the car to make it possible to manually maneuver the car over our track.

Based on your requirements you may modify this code slightly to provide more or less control. We would be commenting the code as much as possible so as to make it easy to read and understand.

IMPROVEMENTS REQUIRED :

- Initial connection establishment takes sometime(upto a minute)
- First start the web server application and make sure to RESET the arduino every time before you start it.
- On starting, the module picks up some garbage values and hence a few power impulses are picked up by the throttle motor(3-4 times). So be sure to hold the car and lift the hind wheels till connection is established.